## Slide 1: Kitchen Safety Guide
Project code: MWH01a-22
Supervisor: Professor Mow Wai Ho
Author: CHUI, Chi To Anson; CHUNG, Wai Lok; CHOY, Yu Hin

## Slide 2: Background/Problem
Kitchen safety is a high-profile issue
Unattended fire will cause serious potential dangers
Not enough household affordable kitchen safety equipment
Most of the recent equipments include expensive sensor and parts
The image recognition technology is becoming more accurate during the period of covid-19
AI model is applied to our project to lower the price of product

## Slide 3: Recent kitchen safety product
Thermal imaging for improving kitchen safety
iGuardStove (A system make use of different kinds of sensors to measure the environment of the kitchen)
Fall detection system by thermal and depth cameras

## Slide 4: Aim
Demonstrate the feasibility of using RGB cameras with AI to detect stove fires in a kitchen
Provide an effective method for detecting and preventing stove fires, potentially saving lives and preventing significant property damage

## Slide 5: Product description
an Raspberry Pi AI-embedded surveillance system
An Object Detection Module which can identify a human, hand, fire, and cooking utensils (e.g. pot)
Unattended cooking algorithm which can identify unattended cooking event

## Slide 6: System
Data input: NumPy array from MIPI RGB camera
Pre-process:
Resize, brightness, contrast and normalization
Inference: A custom AI YOLOv5 model for individually detecting fire, human, hand and pot
Algorithm: A danger score determined by the existence of each object
Output: audio output (optional video display)

## Slide 7: Objective
Object Detection Framework
Unattended Cooking Algorithm
Hardware system to support the software

## Slide 8: Object Detection Module
Using YOLOv5 Github Repository
Create customized dataset
Training AI weight with customized dataset

## Slide 9: YOLOv5
Open-Source Repository by Ultralytics
  Power by Pytorch
  Functionality: train.py, detection.py, export.py, etc.

## Slide 10: Create Dataset
Collecting Image
  Online image + Self-recorded clips
Labeling
  Using Roboflow for Dataset management

## Slide 11: Training AI with processed dataset
In Google Colab Environment (.ipynb)

## Slide 12: Training AI with processed dataset
First Train

## Slide 13: Training AI with processed dataset
Second Train

## Slide 14: Unattended Cooking Algorithm
Version 1: Logic representation of unattended cooking event

## Slide 15: Unattended Cooking Algorithm
Version 2: real-time weighted score
  e.g. currentScore = (fire * 2 + hand * 0.75 + human * 1 + pot * 1.2)
Version 3: forgetful weighted score
  e.g. currentScore = currentScore * 0.5 + (fire * 4 + hand * 0.75 + human * 1 + pot * 1.2)
Version 4: “forgetful” weighted score with negative weights

## Slide 16: Unattended Cooking Algorithm
Version 5: Zero-sum Algorithm
pastScore = currentScore > 0 ? currentScore * 0.5 : 0 currentScore = pastScore + (fire * 0.3 - (hand or human) * 0.5 + pot * 0.2) currentScore = currentScore > 0 ? currentScore : 0

## Slide 17: Problem of algorithms explained (Why we update our algorithm)
Version 1
  It did not emphase the importance of fire
Version 2
  Blocking “fire” does not means there is no fire
Version 3
  High warm-up time
Version 4
  enlarging value over time

## Slide 18: Implementation

## Slide 19: Building of hardware system

## Slide 20: Further discussion and improvement
False positive and false negative
  more images of “human” labels and “hand” labels
  introduce images fom the camera to be implemented (i.e. from MIPI camera)
Slow processing rate
  AI model format
  hardware improvement / hardware acceleration

## Slide 21: Chui’s Work

## Slide 22: Chung’s Work
AI training and database management
  deduplication of input images
  Training on Google Colab
  Proving the usefulness by testing against video

## Slide 23: Choy’s Work
-Collect dataset
-setting up the camera and raspberry pi